## Slide 1
BLIND CANE
TRAINING SYSTEM
A Gamified Approach to White Cane Navigation Training
Mechatronics Senior Project | Spring 2026

## Slide 2
The Problem
No Real-Time Feedback
Instructors give verbal corrections after the fact. Students can’t tell in the moment if technique is correct.
Unmeasurable Progress
No quantitative tracking. Sessions rely on subjective observation with no data to compare across days.
Repetitive & Unengaging
Traditional drills are monotonous. No sense of achievement, progression, or reward for improving.
Limited Scalability
Requires dedicated 1-on-1 time with a certified specialist. Sessions are expensive and hard to schedule.
How do we make cane training measurable, engaging, and self-guided?

## Slide 3
Our Solution
A sensor-equipped cane that gives real-time haptic and audio feedback, turning cane training into a skill-progression game.
Smart Cane
IMU + Ultrasonic
Haptic motors
Color marker
Propeller P2
8-cog real-time
sensor fusion
haptic + audio
Laptop
Python + OpenCV
game engine
serial to P2
TV Display
Live AR overlay
for observers
post-run debrief
▶
▶
▶
Ceiling Camera — tracks player via color marker on cane
Key constraint: The player is blindfolded. ALL feedback is haptic (vibration) and audio (earpiece).
The TV display is for instructors and observers only.

## Slide 4
System Architecture
Ultrasonic Sensor
IMU / Accelerometer
Haptic Motors
Propeller P2
8 Cogs
Real-time
Laptop
Python + OpenCV
Game Engine
Scoring + AR
TV Display
AR Overlay
Ceiling Cam
Color Track
Serial USB
HDMI
USB

## Slide 5
The Smart Cane
HC-SR04 Ultrasonic
Mounted 3–4 inches from tip, 90° to shaft. Detects obstacles 0.2–1.5m ahead.
MPU-6050 IMU
Inside handle, near grip. Measures sweep arc width, tempo, and rhythm.
ERM Vibration Motors
1–2 coin motors in grip area. Distinct pulse patterns for each feedback type.
Color Marker
Bright tape on cane tracked by ceiling camera via OpenCV HSV thresholding.
Propeller P2 — 8 Cog Architecture
Cog 0: Ultrasonic ping loop
Cog 1: IMU reader + technique grader
Cog 2: Force sensor + tap detector
Cog 3: Position stream from laptop
Cog 4: Game state machine
Cog 5: Audio engine (I2S/PWM)
Cog 6: Haptic pattern sequencer
Cog 7: Serial link to laptop
Why Parallel Processing?
Every sensor has strict timing. Ultrasonic needs µs precision. Audio glitches if interrupted. Haptics must run independently. Sequential processing = unacceptable latency.

## Slide 6
Computer Vision Pipeline
1
Calibrate
Click marker to sample HSV color. Adjust tolerance.
2
Threshold
Convert to HSV. inRange mask. Erode + dilate.
3
Detect
Find largest contour. Compute centroid via moments.
4
Track
Feed (x,y) to game engine. ~30 FPS update rate.
▶
▶
▶
Why Color Tracking Instead of ArUco?
ArUco markers need a minimum printed size to be reliably detected by a ceiling camera at room height. A small piece of colored tape has no size constraint — HSV thresholding detects it regardless of apparent size in frame. Calibration takes 2 clicks and adapts to any lighting condition.

## Slide 7
The Four Training Pillars
Each pillar trains a distinct cane skill with 3 progressive difficulty levels
1
Rhythm
Refiner
Cane sweep technique.
Arc width, tempo,
ground contact.
2
Hazard
Course
Obstacle detection
and avoidance using
ultrasonic feedback.
3
Memory
Run
Learn a route, then
retrace from pure
spatial memory.
4
Carto-
grapher
Explore unknown space.
Build mental map.
Recall object locations.

## Slide 8
Pillar 1 — Rhythm Refiner
IMU grades every sweep cycle on three axes
Arc Width
Left-to-right range
Tempo
Time between sweeps
Ground Contact
Tip touches floor
Grading
A
All axes within tolerance
B
One axis slightly off
C
Two axes off
F
Sweep barely recognizable
Levels
L1
Straight Line Drill
Walk A→B at 60 BPM
L2
Tempo Run
60→75→90 BPM acceleration
L3
Technique Gauntlet
A-grade through obstacle course

## Slide 9
Pillar 2 — Hazard Course
Ultrasonic drives haptic proximity ramp — closer = stronger vibration
>1.5m
None
1.5–1.0m
Gentle
1.0–0.5m
Medium
0.5–0.2m
Strong
<0.2m
Continuous
L1: Single Obstacle
One foam block, open path. Learn to read the proximity ramp.
L2: Corridor Run
Narrow channel, 3 staggered obstacles, 45s timer. Filter wall from obstacle readings.
L3: Dense Grid
7+ obstacles, no predefined path. Read subtle intensity gradients to find gaps.

## Slide 10
Pillar 3 — Memory Run ★
Demo day showpiece — the cognitive challenge that impresses
Phase 1: LEARN
System walks player through the route with full audio narration. Each checkpoint has a unique sound signature. Haptic pulses mark arrivals. Player builds spatial and body memory of the path.
Phase 2: RECALL
All checkpoints hidden. Player retraces route from memory alone. Camera tracks recalled path vs taught path. TV shows both overlaid in real time. On L3: ALL feedback disabled — complete silence.
▶
L1: 3 checkpoints, audio cues during recall L2: 4 checkpoints, walk forward then REVERSE L3: 5 checkpoints, ALL feedback disabled. Pure memory.

## Slide 11
Pillar 4 — Cartographer
Build your own mental map, then prove you remember it
Phase 1: EXPLORE
Free movement, no set path. Objects announce themselves via audio when cane gets close. Player discovers and mentally catalogs each location. Timer counts down.
Phase 2: QUIZ
"Navigate to Object Alpha." Player walks to named objects from memory. Scored on arrival accuracy. Must navigate object-to-object using relative spatial reasoning.
▶
TV: Fog of War — audience sees a dark map that reveals as the player explores. During quiz, objects vanish. Random layouts = infinite replayability.

## Slide 12
Scoring & Progression
Every point maps to a real skill — no filler XP
Event | XP | Sensor
Clean avoidance | +15 | Ultrasonic
Near-miss (<20cm) | +25 | Ultrasonic
Checkpoint in order | +50 | Camera
Perfect sweep (A) | +5 | IMU
Flawless run | +500 | All
Collision | -25 | Force sensor
Technique <C for 5+ | -10 | IMU
Combo Multipliers
x2 5 clean passes in a row
x3 Perfect technique + zero collisions
Unlock System
L1: Always available
L2: Complete L1 in same pillar
L3: Complete L2 with B+ avg
Pillars unlock independently

## Slide 13
Software Prototypes & Testing
Color Tracker
OpenCV HSV calibration + real-time marker tracking. Click-to-sample workflow with adjustable tolerance.
Finger Sweep Trainer
Webcam Pillar 1 prototype. Skin-color detection tracks fingertip. Grades arc + tempo against metronome.
Memory Run + Cartographer
Pillar 3 & 4 prototype using color tracker. Learn/recall phases, fog of war, checkpoint scoring, random layouts.
Pathfinder Firmware
Teammate’s P1 cane firmware: 4 modes (sweep, touch, shoreline, ground). IMU + 3 ultrasonics + 3 haptic motors.

## Slide 14
Live Demo Preview
What you’re about to see
1
Straight Line Drill
Pillar 1 L1 — sweep technique grading
~2 min
2
Single Obstacle
Pillar 2 L1 — ultrasonic + haptic ramp
~2 min
3
Corridor Run
Pillar 2 L2 — timed, 3 obstacles
~3 min
4
Three-Point Route
Pillar 3 L1 — learn then recall
~4 min
5
Silent Run ★
Pillar 3 L3 — ALL feedback off. Pure memory.
~5 min
Total demo time: 15–20 minutes | Questions welcome before and after